# NORTH CAROLINA

# MODEL WIRELESS TELECOMMUNICATIONS ORDINANCE

# [COMPLIES WITH G.S. § xxx {SB831}, EFFECTIVE 12/1/07]

# PCIA, THE WIRELESS INFRASTRUCTURE ASSOCIATION

November 2007

# MODEL WIRELESS TELECOMMUNICATIONS ORDINANCE

I.	Purpose and Legislative Intent.

The purpose of this Wireless Telecommunications Ordinance is to ensure that residents and businesses in [the Municipality] have reliable access to wireless telecommunications networks and state of the art communications services while also ensuring that this objective is achieved in a fashion that preserves the intrinsic aesthetic character of the community and is accomplished according to [the Municipality’s] zoning, planning, and design standards, as expressed in G.S. § xxx [SB831], effective December 1, 2007.  The Telecommunications Act of 1996 preserved, with certain limitations, local government land use and zoning authority concerning the placement, construction, and modification of wireless telecommunications facilities.  [The jurisdicational authority] recognizes that facilitating the development of wireless service technology can be an economic development asset to [the jurisdictional authority] and a significant benefit to its residents.  To accomplish the above stated objectives and to ensure that the placement, construction or modification of wireless telecommunications facilities complies with all applicable Federal laws, and is consistent with [the jurisdictional authority’s] land use policies, [the jurisdictional authority] is adopting a single, comprehensive, wireless telecommunications ordinance.

This Ordinance establishes parameters for the siting of Wireless Telecommunications Facilities.  By enacting this Ordinance it is [the jurisdictional authority’s] intent to:

- Ensure access to reliable wireless communications services throughout all areas of [the Municipality];

- Encourage the use of existing Monopoles, Towers, Utility Poles and other structures for the collocation of  Telecommunications Facilities;

(3)	Encourage the location of new Monopoles and Towers in non-residential areas;

(4)	Minimize the number of new Monopoles and Towers that would otherwise need to be constructed by providing incentives for the use of existing structures;

(5)	Encourage the location of Monopoles and Towers, to the extent possible, in areas where the adverse impact on the community will be minimal;

(6)	Minimize the potential adverse effects associated with the construction of Monopoles and Towers through the implementation of reasonable design, landscaping and construction practices;

(7)	Ensure public health, safety, welfare, and convenience; and

(8)	Conform to Federal and State laws that allow certain antennas to be exempt from local regulations.

II.	Definitions.

For the purposes of this Ordinance, the following terms shall be defined as:

Accessory Equipment -- Any equipment serving or being used in conjunction with a Telecommunications Facility or Support Structure.  This equipment includes, but is not limited to, utility or transmission equipment, power supplies, generators, batteries, cables, equipment buildings, cabinets and storage sheds, shelters or other structures.

Administrative Approval -- Zoning approval that the [Zoning Administrator] or designee is authorized to grant after Administrative Review.

Administrative Review -- The procedures established in Section IV E of this Ordinance.

Antenna – Communications equipment that transmits and receives electromagnetic radio signals used in the provision of all types of wireless communications services..

Application – A formal request submitted to the city or county to construct or modify a wireless support structure or a wireless facility.

Building Permit – An official administrative authorization issued by the city or county prior to beginning construction consistent with the provisions of G.S. 153A-357 and G.S. 160A-417.

Collocation –The installation of new wireless facilities on previously-approved structures, including towers, buildings, utility poles, and water tanks.

“Carrier on Wheels” or “Cell on Wheels” (“COW”) -- A portable self-contained cell site that can be moved to a location and set up to provide personal wireless services on a temporary or emergency basis.  A COW is normally vehicle-mounted and contains a telescoping boom as the Antenna support structure.

Equipment Enclosure – An enclosed structure, cabinet or shelter used to contain radio or other equipment necessary for the transmission or reception of wireless communications signals.

Fall Zone – The area in which a wireless support structure may be expected to fall in the event of a structural failure, as measured by engineering standards.

Land Development Regulation – Any ordinance enacted pursuant to G.S. § xxx [SB831].

Ordinary Maintenance -- Ensuring that Telecommunications Facilities and Support Structures are kept in good operating condition.  Ordinary Maintenance includes inspections, testing and modifications that maintain functional capacity, aesthetic and structural integrity; for example the strengthening of a Support Structure’s foundation or of the Support Structure itself.  Ordinary Maintenance includes replacing Antennas and Accessory Equipment on a like-for-like basis within an existing Telecommunications Facility and relocating the Antennas of approved Telecommunications Facilities to different height levels on an existing Monopole or Tower upon which they are currently located.  Ordinary Maintenance does not include Minor and Major Modifications.

Major Modifications -- Improvements to existing Telecommunications Facilities or Support Structures that result in a substantial change to the Facility or Structure.  Collocation of new Telecommunications Facilities to an existing Support Structure without Replacement of the structure shall not constitute a Major Modification.  Major Modifications include, but are not limited to, extending the height of the Support Structure by more than twenty (20) feet or ten percent (10%) of its current height whichever is greater, and the Replacement of the structure.

Minor Modifications -- Improvements to existing Telecommunications Facilities and Support Structures, that result in some material change to the Facility or Support Structure but of a level, quality or intensity that is less than a “substantial” change.  Such Minor Modifications include, but are not limited to, extending the height of the Support Structure by less than twenty (20) feet or ten percent (10%) of its current height, whichever is greater, and the expansion of the compound area for additional Accessory Equipment.

Monopole --A single, freestanding pole-type structure supporting one or more Antenna.  For purposes of this Ordinance, a Monopole is not a Tower.

Replacement -- Constructing a new Support Structure of proportions and of equal height or such other height as would be allowed under the definition of Minor Modification to a pre-existing Support Structure in order to support a Telecommunications Facility or to accommodate Collocation and removing the pre-existing Support Structure.

Search Ring – The area within which a wireless facility must be located in order to meet service objectives of the wireless service provider using the wireless facility or wireless support structure.

Stealth Telecommunications Facility -- Any Telecommunications Facility that is integrated as an architectural feature of a structure so that the purpose of the Facility for providing wireless services is not readily apparent to a casual observer.

Support Structure(s) – A structure designed to support Telecommunications Facilities including, but not limited to, Monopoles, Towers, Utility Poles and other freestanding self- supporting structures.

Tower -- A lattice-type structure, guyed or freestanding, that supports one or more Antennas.

Utility Pole – A structure that is designed for and used to carry lines, cables, or wires for telephone, cable television, or electricity, or to provide lighting.

Wireless Facility – The set of equipment and network components, exclusive of the underlying support structure or tower, including antennas, transmitters, receivers, base stations, power supplies, cabling, and associated equipment necessary to provide wireless data and telecommunications services to a discrete geographic area.

Wireless Support Structure – A new or existing structure, such as a monopole, lattice tower, or guyed tower that is designed to support or capable of supporting wireless facilities.  A utility pole is not a wireless support structure.

III.	Approvals Required for Telecommunications Facilities and Support Structures.

(A)	Administrative Review.  Wireless Facilities located on any existing  support structure shall be permitted in any zoning district after Administrative Review and Administrative Approval in accordance with the standards set forth in this Ordinance.  New Support Structures that are less than sixty (60) feet in height shall be permitted in any zoning district after Administrative Review and Administrative Approval in accordance with the standards set forth in this Ordinance.  New Support Structures up to one hundred ninety-nine (199) feet in height shall be permitted in any Industrial District after Administrative Review and Administrative Approval in accordance with the standards set forth in this Ordinance.  Monopoles or replacement poles located in utility easements or rights-of-way shall be permitted in any zoning district after Administrative Review and Administrative Approval in accordance with the standards set forth in this Ordinance.  Stealth Telecommunications Facilities shall be permitted in any zoning district after Administrative Review and Administrative Approval in accordance with the standards set forth in this Ordinance.

(B)	Special Permit.  Wireless Facilities and Support Structures not permitted by Administrative Approval shall be permitted in any district upon the granting of a Special Permit from the [Zoning Board] in accordance with the standards set forth in this Ordinance.

(C)	Exempt.  Ordinary Maintenance of existing Wireless Facilities and Support Structures, as defined herein, shall be exempt from zoning and permitting requirements.  In addition,  the following facilities are not subject to the provisions of this Ordinance: (1) antennas used by residential households solely for broadcast radio and television reception ; (2) satellite antennas used solely for residential or household purposes;  (3) COWs placed for  a period of not more than one hundred twenty (120) days at any location within [The Municipality] after a declaration of an emergency or a disaster by the Governor or by the responsible official of [The Municipality]; and (4) television and AM/FM radio broadcast towers and associated facilities.

IV.	Collocation Permitted by Administrative Approval.

A.	Collocation

- Applications for Collocation entitled to Administrative Review under G.S. § xxx [SB831] shall be reviewed for conformance with applicable site plan and building permit requirements but shall not otherwise be subject to zoning requirement, including design or placement requirements, or public hearing review.

- Applications for Collocation of Wireless Facilities are entitled to Administrative Reivew if the addition of the additional Wireless Facility does not exceed the number of wireless facilities previously approved for the wireless support structure on which the Collocation is proposed and meets all the requirements and conditions of the original approval.  This provision applies to Wireless Support Structures which are approved on or after December 1, 2007.

- Administrative Review process set forth in Section IV (E) of this Ordinance shall apply to all Collocations, in addition to collocations qualified for streamlined processing under subjections (1) and (2) of this section, that meet the following requirements:

- The Collocation does not increase the overall height and width of the Tower or Wireless Support Structure to which the Wireless Facilities are to be attached.

- The Collocation does not increase the ground space area approved in the site plan for Equipment Enclosures and Accessory Structures.

- The Wireless Facilities in the proposed Collocation comply with applicable regulations, restrictions, or conditions, if any, applied to the initial Wireless Facilities placed on the Tower or other Wireless Support Structure.

- The additional Wireless Facilities comply with all federal, state and local safety requirements.

- The Collocation does not exceed the applicable weight limits for the Wireless Support Structure.

- Antennas and Accessory Equipment are permitted in all zoning districts when located on any existing structure, including, but not limited to, buildings, water tanks, utility poles, broadcast towers or any existing Support Structure in accordance with the requirements of this Part.

(5)	Antennas and Accessory Equipment may exceed the maximum building height limitations, provided the Antenna and Accessory Equipment are in compliance with the requirements and standards of this section.

(6)	Each Antenna mounted on existing structures and any Accessory Equipment shall meet the following standards:

(a)	Omnidirectional or whip Antennas shall not exceed twenty (20) feet in length and not exceed seven (7) inches in diameter and shall be of a color that is identical or similar to the color of the supporting structure to make the Antenna and related Accessory Equipment visually unobtrusive.

(b)	Directional or panel Antennas shall not exceed ten (10) feet in length and two (2) feet in width and shall be of a color that is identical or similar to the color of the supporting structure to make the Antenna and related Accessory Equipment visually unobtrusive.

- Cylinder-type Antennas shall not exceed ten (10) feet in length and not exceed twelve (12) inches in diameter and shall be of a color that is identical or similar to the color of the supporting structure to make the Antenna and related Accessory Equipment visually unobtrusive.

- Satellite and microwave dishes shall not exceed ten (10) feet in diameter.  Dish antennas greater than three (3) feet in diameter shall be screened with an appropriate architectural treatment that is compatible with or integral to the architecture of the building to which they are attached.  This screening requirement shall not apply to dishes located upon Towers or Monopoles.

- Other Antenna types not specifically mentioned above shall be permitted if they are not significantly greater in size and will have a visual impact no greater than the Antennas listed above.  This provision is specifically included in this Ordinance to allow for future technological advancements in the development of Antennas.

(f)	Accessory Equipment must comply with Section VI (E).

B.	New Support Structures

(1)	New Support Structure less than fifty (60) feet in height shall be permitted in all zoning districts in accordance with the requirements of this Part.

(2)	New Support Structures up to one hundred ninety-nine (199) feet in height shall be permitted in all Industrial Districts in accordance with the requirements of this Part.  The height of any proposed support structure shall not exceed the minimum height necessary to meet the coverage objectives of the Facility.  The setback of the structure shall be governed by the setback requirements of the underlying zone.

(3)	In the case of a monopoles or replacement poles that will support utility lines as well as a Telecommunications Facility shall be permitted within utility easements or rights-of-way, in accordance with requirements of this Part.

(a)	The utility easement or right-of-way shall be a minimum of one hundred (100) feet in width.

(b)	The easement or right-of-way shall contain overhead utility transmission and/or distribution structures that are eighty (80) feet or greater in height.

(c)	The height of the Monopole or replacement pole may not exceed by more than thirty (30) feet the height of existing utility support structures.

(d)	Monopoles and the Accessory Equipment associated there with shall be set back a minimum of fifteen (15)feet from all boundaries of the easement or right-of-way.

(e)	Single carrier Monopoles may be used within utility easements and rights-of-way due to the height restriction imposed by Subsection (c) above.

(f)	Poles that use the structure of a utility tower for support are permitted under this Section.  Such poles may extend up to twenty (20) feet above the height of the utility tower.

(4)	Monopoles or replacement poles located on public property or within public rights-of-way that will support public facilities or equipment in addition to Telecommunications Facilities shall be permitted in accordance with requirements of this Part.  Examples include, but are not limited to, municipal communication facilities, athletic field lights, traffic lights, street lights, and other types of utility poles in the public right-of-way.

C.	Stealth Telecommunications Facilities

(1)	Stealth Telecommunications Facilities shall be permitted in all zoning districts after Administrative Review and Administrative Approval in accordance with the requirements below:

(a)	Antennas must be enclosed, camouflaged, screened, obscured or otherwise not readily apparent to a causal observer.

- The structure utilized to support the Antennas must be allowed within the underlying zone district.  Such structures may include, but are not limited to, flagpoles, bell towers, clock towers, crosses, monuments, smoke stacks, parapets, and steeples.

- Setbacks for the supporting structure shall be governed by the setback requirements of the underlying zoning district.

D.	General Standards, Design Requirements, and Miscellaneous Provisions

(1)	Unless otherwise specified herein, all Telecommunications Facilities and Support Structures permitted by Administrative Approval are subject to the applicable general standards and design requirements of Section VI and the provisions of Section VII.

E.	Administrative Review Process

  - All Administrative Review applications must contain the following:

(a)	Administrative Review application form signed by applicant.

(b)	Copy of lease or letter of authorization from property owner evidencing applicant’s authority to pursue zoning application

(c)	Zoning Drawings detailing proposed improvements.  Drawings must depict improvements related to the requirements listed in this Part, including property boundaries, setbacks, topography, elevation sketch, and dimensions of improvements.

(d)	In the case of a new Support Structure:

- Statement documenting why collocation cannot meet the applicant's requirements.  Such statement may include such technical information and other justifications as are necessary to document the reasons why collocation is not a viable option; and

- The applicant shall provide a list of all existing structures considered as alternatives to the proposed location.  The applicant shall provide a written explanation why the alternatives considered were either unacceptable or infeasible due to technical, physical, or financial reasons.  If an existing tower or monopole is listed among the alternatives, applicant must specifically address why the modification of such structure is not a viable option.

- Applications for new Support Structures with proposed Telecommunications Facilities shall be considered together as one application requiring only a single application fee.

(e)	Administrative Review application fee.

  - Procedure.

(a)	A Collocation application entitled to Administrative Review under G.S. § xx [SB831] shall be deemed complete unless the city or county provides notice in writing to the applicant within forty-five (45) days of submission or within some other mutually agreed upon timeframe.  The notice shall identify the deficiencies in the application which, if cured, would make the application complete.  The application shall be deemed complete on resubmission if the additional materials cure the deficiencies identified.

(b)	An applicant that receives notice of an incomplete application may submit additional documentation to complete the application.  An applicant’s failure to complete the application within sixty (60) business days after receipt of written notice shall constitute a withdrawal without prejudice of the application.  An application withdrawn without prejudice may be resubmitted upon the filing of a new application fee.

(c)	The Administrative Review meeting will be conducted to confirm that the proposed application is consistent with this Ordinance.  The [Zoning Administrator] must issue a written decision granting or denying the request within forty-five (45) days of the meeting unless an extension of time is agreed to by the Applicant.  Failure to issue a written decision within forty-five (45)  days shall constitute a denial of the application.  The applicant may appeal such a denial as provided in this Ordinance or applicable State or Federal Law.

(d)	Should the [Zoning Administrator] deny the application, the [Zoning Administrator] shall provide written justification for the denial.  The denial must be based on substantial evidence of inconsistencies between the application and this Ordinance.

(e)Applicant may appeal  any decision of the [Zoning Administrator] approving, approving with conditions, or denying an application or deeming an application incomplete, within thirty (30) days to [the Local Appeals Board] in accordance with this Ordinance.

- The [jurisdictional authority] may fix and charge an application fee, consulting fee, or other fee associated with the submission, review, processing, and approval of an application to site or modify Wireless Facilities or Wireless Support Structures that is based on the costs of the services provided and does not exceed what is usual and customary for such services.  Any charges or frees assessed by [jurisdictional authority] on account of an outside consultant shall be fixed in advance and incorporated into a permit or application fee and shall be based on the reasonable costs to be incurred by [jurisdictional authority] in connection with the regulatory review authorized under this Ordinance.  The foregoing does not prohibit [jurisdictional authority] from imposing additional reasonable and cost-based fees for costs incurred should an applicant amend its application.  On require, the amount of the consultant charges incorporated into the permit or application fee shall be separately identified and disclosed to the applicant.

- The [jurisdictional authority] many not require the placement of Wireless Support Structures or Wireless Facilities on property owned or leased by [jurisdiction], but may develop a process to encourage the placement of Wireless Support Structures or facilities on property owned or leased by [jurisdiction], including an expedited approval process.

V.	Telecommunications Facilities and Support Structures Permitted by Special Permit.

A.	Any Telecommunications Facility or Support Structures Not Meeting the Requirements of Section IV Shall Be Permitted by Special Permit in all Zoning Districts Subject to:

(1)	The submission requirements of Section V (B) below; and

(2)	The applicable standards of Sections VI and VII below; and

(3)	The requirements of the special permit general conditions at Code Section  ____.  [Insert cross reference to Municipality code section that establishes general conditions applicable to Special Permits.]

B.	Submission Requirements for Special Permit Applications

(1)	All Special Permit applications for Telecommunications Facility and Support Structures must contain the following:

- Special Permit application form signed by applicant.

- Copy of lease or letter of authorization from the property owner evidencing applicant’s authority to pursue zoning application.

(b)	Written description and scaled drawings of the proposed Support Structure, including structure height, ground and structure design, and proposed materials.

(c)	Number and type of proposed Antennas and their height above ground level, including the proposed placement of Antennas on the Support Structure.

(d)	When locating within a residential area, a written technical and operational analysis of why a Monopole or similar structure at a height of less than one hundred (100) feet cannot be used.

(e)	Line-of-sight diagram or photo simulation, showing the proposed Support Structure set against the skyline and viewed from at least four (4) directions within the surrounding areas.

(f)	A statement justifying why Collocation is not feasible.  Such statement shall include:

(i)	Such technical information and other justifications as are necessary to document the reasons why collocation is not a viable option; and

(ii)	The applicant shall provide a list of all existing structures considered as alternatives to the proposed location.  The applicant shall provide a written explanation why the alternatives considered were either unacceptable or infeasible due to technical, physical, or financial reasons.  If an existing tower was listed among the alternatives, applicant must specifically address why the modification of such tower is not a viable option.

(g)	A statement that the proposed Support Structure will be made available for Collocation to other service providers at commercially reasonable rates.

(h)	If required of other Special Permit applications, a property owner list that includes the name, address, and tax parcel information for each parcel entitled to notification of the application.

(j)	Special Permit application fee.

(C)	Procedure.

(1)	Within ten (10) business days of the receipt of an Application for a Special Permit, the [Zoning Administrator or the Zoning Board’s designee] shall meet with the applicant to confirm that the application is complete or to inform the applicant in writing the specific reasons why the application is incomplete.  This review meeting with staff is not a public hearing and is not subject to any public notification requirements.

(2)	If an application is deemed incomplete, an Applicant may submit additional materials to complete the application.  An applicant’s failure to complete the application within sixty (60) business days after receipt of written notice shall constitute a withdrawal without prejudice of the application.  An application withdrawn without prejudice may be resubmitted upon the filing of a new application fee.

(3)	Once an application is deemed complete, a review meeting shall be held within ten (10) days.

(4)	At this review meeting, staff shall provide applicant, in writing, a list of additional potential alternative structures, including readily-available identifying information (e.g., address, tax map identification, latitude and longitude) or such other information as will allow the applicant to identify the potential alternative structures.  If, after investigation, the applicant concludes that the potential alternative structures identified by municipal staff are not acceptable or feasible, the applicant shall provide an explanation for its decision using technical, physical, or financial information at the hearing on the Special Permit.   [Jurisdictional authority] shall not deny an initial approval based on such documentation.

(5)	A complete application for a Special Permit shall be scheduled for a hearing date at this review meeting in accordance with the requirements of this Ordinance.

(6)	Applications for new Support Structures with proposed Telecommunications Facilities shall be considered as one application requiring only a single application fee.

(7)	The posting of the property and public notification of the application shall be accomplished in the same manner required for any Special Permit application under this Ordinance.

VI.	General Standards and Design Requirements.

(A)	Design.

(1)	Monopoles shall be subject to the following:

(a)	Monopoles shall be designed to accommodate at least three (3) telecommunications providers.

(b)	The compound area surrounding the Monopole must be of sufficient size to accommodate Accessory Equipment for at least three (3) telecommunications providers.

(c)	Unless otherwise required by the Federal Communications Commission, the Federal Aviation Administration, or [the Municipality], Monopoles shall have a galvanized silver or gray finish.

(2)	Towers shall be subject to the following:

(a)	Towers shall be designed to accommodate at least four (4) telecommunications providers.

(b)	A compound area surrounding the Tower must be of sufficient size to accommodate Accessory Equipment for at least four (4) telecommunications providers.

(c)	Unless otherwise required by the Federal Communications Commission, the Federal Aviation Administration, or [the Municipality], Towers shall have a galvanized silver or gray finish.

  - Stealth Telecommunications Facilities shall be designed to accommodate the Collocation of other Antennas whenever economically and technically feasible or aesthetically appropriate, as determined by the [Zoning Board] or [Zoning Administrator].

  - Upon request of the Applicant, the [Zoning Board or Zoning Administrator] may waive the requirement that new Support Structures accommodate the collocation of other service providers if it finds that collocation at the site is not essential to the public interest, or that the construction of a shorter support structure with fewer Antennas will promote community compatibility.

(B)	Setbacks.

- Property Lines.  Unless otherwise stated herein, Monopoles and Towers shall be setback from all property lines a distance equal to their height measured from the base of the structure to its highest point.  Other Support Structures shall be governed by the setbacks required by the underlying zoning district.

- Residential Dwellings.  Unless otherwise stated herein, Monopoles, Towers and other Support Structures shall be setback from all off-site residential dwellings a distance equal to the height of the structure.  There shall be no setback requirement from dwellings located on the same parcel as the proposed structure.  Existing or Replacement utility poles shall not be subject to a set back requirement.

- Unless otherwise stated herein, all Accessory Equipment shall be setback from all property lines in accordance with the minimum setback requirements in the underlying zoning district.  Accessory Equipment associated with an existing or Replacement utility pole shall not be subject to a set back requirement.

- The [Zoning Board or Zoning Administrator] shall have the authority to reduce or waive any required setback upon the request of the applicant if the Telecommunications Facility or Support Structure will be less visible as a result of the diminished setback.  The [Zoning Board or Zoning Administrator] must also find that the reduction or waiver of the setback is consistent with the purposes and intent of this Ordinance.  The structure must still meet the underlying setback requirements of the zone.

(C)	Height

- In non-residential districts, Support Structures shall not exceed a height of one hundred ninety-nine (199) feet from the base of the structure to the top of the highest point.  Any proposed Support Structure shall be designed to be the minimum height needed to meet the service objectives of the applicant.

- In residential districts, Support Structures shall not exceed a height equal of one hundred fifty (150) feet from the base of the structure to the top of the highest point.  Any proposed Support Structure shall be designed to be the minimum height needed to meet the service objectives of the applicant.

- In all districts, the [Zoning Board] shall have the authority to reduce or waive the height restrictions listed in this section upon the request of the applicant and a satisfactory showing of need for a greater height.  With its waiver request the Applicant shall submit such technical information or other justifications as are necessary to document the need for the additional height to the satisfaction of the [Zoning Board].

(D)	Aesthetics.

- Lighting and Marking.  Telecommunications Facilities or Support Structures shall not be lighted or marked unless required by the Federal Communications Commission or the Federal Aviation Administration (FAA).

- Signage.  Signs located at the Telecommunications Facility shall be limited to ownership and contact information, FCC antenna registration number (if required) and any other information as required by government regulation.  Commercial advertising is strictly prohibited.

- Landscaping.  In all districts, the [Zoning Board or Zoning Administrator] shall have the authority to impose reasonable landscaping requirements surrounding the Accessory Equipment.  Required landscaping shall be consistent with surrounding vegetation and shall be maintained by the facility owner.  The [Zoning Board or Zoning Administrator] may choose to not require landscaping for sites that are not visible from the public right-of-way or adjacent property or in instances where in the judgment of the [Zoning Board or Zoning Administrator], landscaping is not appropriate or necessary.

(E)	Accessory Equipment, including any buildings, cabinets or shelters, shall be used only to house equipment and other supplies in support of the operation of the Telecommunication Facility or Support Structure.  Any equipment not used in direct support of such operation shall not be stored on the site.

(1)	An equipment building, shelter or cabinet must not exceed five hundred sixty (560) square feet and twelve (12) feet in height, including the support structure for the equipment building.

(i)	Exception to size restriction.  A single equipment building or shelter may exceed five hundred sixty (560) square feet, if it:  is located at ground level; is used by more than one telecommunication provider; and does not exceed one thousand five hundred (1500) square feet.

(ii)	Exception to height restriction.  Upon the Applicant’s request, the [Zoning Board or Zoning Administrator] may waive the height restriction to allow for the stacking of equipment on top of each other.  The [Zoning Board or Zoning Administrator] must find that there is a practical necessity for the stacking of the equipment and that any resulting impact on adjoining properties is minimal or may be minimized by the requiring of appropriate screening.  [The Zoning Board or Zoning Administrator] may also waive the height restriction where a higher support structure is needed to raise the Equipment above  a slope or flood plains.

(2)	If the Accessory Equipment is at ground level in a residential zone, the [Zoning Board or Zoning Administrator] may require that the building or shelter be faced with brick or other suitable material on all sides and that the compound area be surrounded by landscaping providing a screen of at least three (3) feet in height at installation.  The Accessory Equipment must conform to the setback standards of the applicable zone.  In the situation of stacked equipment buildings, additional screening/landscaping measures may be required by the [Zoning Board or Zoning Administrator].

## VII.	Miscellaneous Provisions.

(A)	Safety.

- Ground mounted Accessory Equipment and Support Structures shall be secured and enclosed with fence not less than six (6) feet in height as deemed appropriate by the [Zoning Board] or [Zoning Administrator].

- The [Zoning Board or Zoning Administrator] may waive the requirement of Subsection (1) above if it is deemed that a fence is not appropriate or needed at the proposed location..

(B)	Abandonment and Removal.

- Abandonment.  Any Telecommunications Facility or Support Structure that is not operated for a period of twelve (12) consecutive months shall be considered abandoned.

- Removal.  The owner of the Telecommunications Facility or Support Structure shall remove the Facility within six (6) months of its abandonment.  The [Municipal Authority] shall ensure and enforce removal by means of its existing regulatory authority.

(C)	Multiple Uses on a Single Parcel or Lot: Telecommunications Facilities and Support Structures may be located on a parcel containing another principal use on the same site.

## VIII.	Telecommunications Facilities and Support Structures in Existence on the Date of Adoption of this Ordinance.

(A)	Telecommunications Facilities and Support Structures that were legally permitted on or before the date this Ordinance was enacted shall be considered a permitted and lawful use.

(B)	Non-Conforming Telecommunications Facility.

(1)	Non-conforming Antennas or Accessory Equipment:  Ordinary Maintenance may be performed on Non-conforming Antennas and Accessory Equipment.

(2)	Minor Modifications to non-conforming Telecommunications Facilities may be permitted upon the granting of Administrative Approval by the [Zoning Administrator].

(3)	Major Modifications to non-conforming Telecommunications Facilities may be permitted only upon the granting of Special Permit approval by the [Zoning Board].

(C)	Non-Conforming Support Structures.

(1)	Non-conforming Support Structure:  Ordinary Maintenance may be performed on a Non-conforming Support Structure.

(2)	Collocation of Telecommunications Facilities on an existing non-conforming Support Structure is permitted upon the granting of Administrative Approval by the Zoning Administrator.

(3)	Minor Modifications may be made to non-conforming Support Structures to allow for Collocation of Telecommunications Facilities.  Such Minor Modifications shall be permitted by Administrative Approval granted by the [Zoning Administrator].

- Major Modifications may be made to non-conforming Support Structures only upon the granting of Special Permit approval by the [Zoning Board].

For Further Questions Please Contact:

Jackie McCarthy

Director of Government Affairs

PCIA/The Wireless Infrastructure Association

The DAS Forum

500 Montgomery Street, Suite 700

Alexandria, VA 22314

(703) 739-0300

mccarthyj@pcia.com

# Comments

As a general question, should provisions regarding new structures be included in our NC model ordinance?  New structures are not specifically addressed in SB831, but I will leave in all references to new structures throughout the remainder of this ordinance. --Jackie

Should we remove this? -- Jackie

Should this be removed?  --Jackie